## Slide 1
Design and Implementation of a Manchester Encoding System
Project Presentation of Electronic Communication Sessional.

## Slide 2
Team Members
Arpan Paul Sanju
ID: 2102021
Meherin Mashri Nijum
ID: 2102023
Abir Ahmed
ID: 2102024
Md. Anas Bin Hossain
ID: 2102029

## Slide 3
What is Encoding?
The process of converting information from one form to another.
LINE CODING is a specific type of Encoding.
Converts binary data (0s and 1s) into electrical/optical signals.
Line coding is the process of converting digital data into digital signals for transmission.

## Slide 4
Line Coding in Communication

## Slide 5
What is Manchester Encoding?
Definition: A synchronous clock-encoding technique that combines data and clock signals into one bitstream.
Self-Clocking: The clock signal is embedded in the data, eliminating need for separate clock line.
Transition-Based: Data is represented by transitions (high-to-low or low-to-high) at bit center.
IEEE 802.3 Standard: Logic 0 = high-to-low transition; Logic 1 = low-to-high.
G.E. Thomas Convention: Logic 0 = low-to-high; Logic 1 = high-to-low transition.

## Slide 6
G.E. Thomas Convention & IEEE 802.3 Ethernet Standard

## Slide 7
NRZ-L & RZ

## Slide 8
The Optimal Hybrid Solution
Inherits Best of Both:
From NRZ-L: Only 2 voltage levels → Simple
Implementation From RZ: Guaranteed mid-bit transitions → Perfect clock synchronization
Eliminates Worst Problems:
NRZ-L's Flaw: No transitions during long runs → Clock sync lost
RZ's Flaw: 3 voltage levels needed → Complex, bandwidth-heavy

## Slide 9
How Manchester Encoding Works
XOR Operation: Manchester = Data XOR Clock.
Guaranteed Transitions: At least one transition per bit period ensures clock recovery.
No DC Component: Signal does not stay at high or low for extended periods.
Better Synchronization: Receiver can extract timing information from transitions.

## Slide 10
Arduino Implementation Setup
Microcontroller: Arduino UNO.
Serial Communication: 9600 baud.
Output: Serial Plotter visualization.
Clock Frequency: 1 Hz (1 second period).
Data Update Rate: Every 1 second.

## Slide 11
Code Structure & Variables
Key Parameters: Clock toggles every 500ms, data changes every 1 second, enabling clear visualization on Serial Plotter
// Timing parameters (OPTIMIZED FOR VISUALIZATION) const int CLOCK_HALF_PERIOD = 500; // 500ms = 1Hz clock const int DATA_DURATION = 1000; // Change data every 1 second unsigned long lastClockEdge = 0; unsigned long lastDataChange = 0;
int clockState = 0;
int dataBit = 0; (code structure variable)

## Slide 12
Arduino Loop Logic
Process: Clock and data are generated independently, then combined via XOR operation
// 1. Clock Generation (1Hz: 500ms high, 500ms low)
if (now - lastClockEdge >= CLOCK_HALF_PERIOD) {
clockState = !clockState;
lastClockEdge = now;
}
// 2. Data Generation (changes every 1 second)
if (now - lastDataChange >= DATA_DURATION) {
dataBit = !dataBit;
lastDataChange = now;
}
// 3. Manchester Encoding (XOR)
int manchester = dataBit ^ clockState; (Arduino loop logic)

## Slide 13
Serial Data Output
Output Format: Three traces visualized simultaneously with vertical offsets for clarity
// Send to Serial Plotter (with offsets for visualization)
Serial.print(dataBit); // Data (0 or 1)
Serial.print(" ");
Serial.print(clockState + 2); // Clock (2 or 3)
Serial.print(" ");
Serial.println(manchester + 4); // Manchester (4 or 5)
delay(100); // Update every 100ms (serial data output)

## Slide 14
Implementation Steps
Upload code to Arduino UNO via USB cable.
Open Tools → Serial Monitor (9600 baud rate).
Go to Tools → Serial Plotter to visualize signals.
Observe three traces: Data, Clock, and Manchester-encoded output.
Monitor timing of transitions at bit centers.
Verify XOR operation: output matches data ⊕ clock.

## Slide 15
Mathematical Modeling
Manchester encoding is modeled as an Exclusive-OR (XOR) operation. When Data is High (1), the output is the inverse of the Clock.

## Slide 16
Mathematical Modeling
Input Data Bit | Clock Signal | Manchester Encoded Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 17
Serial Plotter Visualization
Blue: Data signal (0-1) | Orange: Clock signal (2-3) | Gray: Manchester output (4-5)

## Slide 18
Bit Value | Transition Type | Description
1 | High-to-Low ↓ | Transition downward at bit center
0 | Low-to-High ↑ | Transition upward at bit center
1 | High-to-Low ↓ | Transition downward at bit center
0 | Low-to-High ↑ | Transition upward at bit center
Encoding Example: Binary "1010"

## Slide 19
Key Concepts Summary
XOR Logic: Manchester = Data ⊕ Clock.
Self-Clocking: Receiver extracts clock from transitions.
Transition Density: High transitions ensure synchronization.
Biphase Code: Each bit encoded as 90° phase shift (positive or negative).

## Slide 20
Key Takeaways
Manchester encoding combines clock and data signals using XOR operation providing self-clocking, error detection, and improved synchronization suitable for digital communication systems and embedded applications.
Arduino Serial Plotter effectively visualizes all three signals simultaneously.

## Slide 21
Key Advantages
✓ Self-Clocking
No separate clock signal needed, reduces wiring complexity.
✓ Error Detection
Missing transitions indicate transmission errors.
✓ AC Coupling
No DC component allows galvanic isolation.
✓ Reliability
Better synchronization and noise immunity.

## Slide 22
Limitations
Bandwidth Overhead: Requires twice the bandwidth of NRZ (Non-Return-to-Zero) encoding.
Lower Data Rate: Only half the data rate of unencoded signals at same frequency.
Power Consumption: Frequent transitions result in higher power consumption.
Distance Limitation: Not suitable for long-distance transmission due to signal attenuation.

## Slide 23
Manchester Encoding
Why It's Reliable
Digital Communication Systems

## Slide 24
Why Manchester Encoding is Reliable
Mid-bit Transitions: Let receiver recover clock and stay synchronized
Sharply Reduces Errors: Minimizes timing errors and bit slips
Fixed Pattern Detection: Transition pattern exposes errors immediately
DC-Balanced: Improves robustness over noisy AC-coupled channels
Real Applications: Used in Ethernet, RFID, and NFC systems

## Slide 25
Summary
Manchester Encoding successfully combines data and clock into a single signal
Arduino implementation demonstrates XOR operation producing synchronized transitions
No separate clock infrastructure needed
Self-clocking property and error detection make it superior for synchronized data transfer
Limitations: 50% bandwidth efficiency loss, higher power consumption, sensitivity to channel noise

## Slide 26
Real-World Applications
Ethernet
10BASE-T and legacy Ethernet networks.
RFID/NFC
Radio frequency identification and near-field communication.
IR Protocols
Infrared remote control systems.
Token Ring
IEEE 802.5 network protocol.
Magnetic Storage
Tape drives and magnetic drum storage.
Space Systems
Voyager spacecraft telemetry.

## Slide 27
Thank You.

## Slide 28
Questions?
Manchester Encoding System - Q&A Session